## Slide 1: The OME-Zarr image data format
Christian Tischer & Erick Ratamero
Data Science Centre, EMBL

## Slide 2: Content day 1
Digital image basics
Image metadata (data type, voxel size, channel info)
Big image data
  Multi-resolution
  Chunking
  Sharding
OME-Zarr
  versions

## Slide 3: Content day 2
Sharing with external collaborators
Remote access for cloud computation
Challenges
Object storage

## Slide 4: Resources
https://zenodo.org/records/17639350/files/Halfway_to_i2k_conference_2025_JohannesSoltwedel.pptx?download=1
https://github.com/zarr-developers/zarr-illustrations-falk-2022
https://docs.google.com/presentation/d/1Bc2G7gnIN7DCjY5N4DuA3bb2uQQCf-xL4aVPvfpS-oA/edit?slide=id.g2a02b0a1836_1_35#slide=id.g2a02b0a1836_1_35

## Slide 6
Index * Calibration = Calibrated coordinate
Origin (0,0)
(0,0)
Image calibration
Notes: Example image: xy_8bit__nucleus_calibrated.tif

## Slide 7
8-bit unsigned integer
00000000 = 0
00000001 = 20 = 1
00000101 = 20 + 22 = 5
11111111 = 20 + 21 + … + 27 = 255
16-bit unsigned integer
1111111111111111 = 20 + 21 + … + 215 = 65535
1000000000000000 = 215 = 32768
0000111111111111 = 20 + 21 + … + 211 = 4095
16-bit signed integer
0000000000000000 = +0
1000000000000000 = -0
1000000000000100 = -4
32-bit floating point
10000001000000000000000000000010 = - 1.? 2?
24-bit RGB
111111110000000001000000 = (255,0,64)
Image datatypes

## Slide 8
011100...10010100101000100000000000001000000000100010101000001010...
0 | 8 | 2 | 42
10 | … | … | …
… | … | … | …
Pixel data start
Pixel data type (bit-depth)
Image dimensions
Compression
Pixel physical size
Microscope name
…
Data
Metadata
Width
Height
Image data layout on your hard-disk

## Slide 9: Image data and metadata example
Plugins > Bio-Formats > Bio-Formats Importer

## Slide 10
Channel 1
Channel 2
Channel 3
Merged/Composite image
X
Y
C
Multi-channel images

## Slide 11
Volumetric images

## Slide 12: OME-TIFF specification for XYZCT image series

## Slide 13
1010101100000000001000000000100010100001010000001010001001000001000101010000010010001011000011010000010010010110000110001001011000
IFD
Pixel data type
Width
Height
Offset to data
Offset to next IFD
…
OME-XML
PixelPhysicalSize
Microscope settings
…
Plane 0: S = 0, Z = 0, T = 0, C = 0
Plane 1: S = 0, Z = 1, T = 0, C = 0
Plane 2: S = 0, Z = 2, T = 0, C = 0
Plane 3: S = 0, Z = 3, T = 0, C = 0
Plane 4: S = 1, Z = 0, T = 0, C = 0
Plane 5: S = 1, Z = 0, T = 0, C = 1
S = Series: Planes belonging to the same “image” with same width, height and data type
TIFF header
Version
Byte order
Offset to first IFD
…
Data
One plane of pixel data
OME-TIFF

## Slide 14: Big image data challenges
Example: A 8 TB volume EM dataset cannot be loaded into your computer’s memory (and if it could it would take a lot of time)

## Slide 15: Multi-resolution and chunking

## Slide 16: OME-Zarr specification for chunked multi-resolution XYZCT images

## Slide 17: OME-Zarr: a chunked file format
Illustration by Henning Falk, licensed under CC-BY 4.0

## Slide 18
0/0 0/1
0/2
0/3
Metadata JSON text files
Down-scale
1/0
"axes": [ {"name": "t", "type": "time", "unit": "millisecond"}, {"name": "c", "type": "channel"}, {"name": "z", "type": "space", "unit": "micrometer"}, {"name": "y", "type": "space", "unit": "micrometer"}, {"name": "x", "type": "space", "unit": "micrometer"} ], "datasets": [ { "path": "0", "coordinateTransformations": [{"type": "scale", "scale": [1.0, 1.0, 0.5, 0.5, 0.5] }] }, { "path": "1", "coordinateTransformations": [{"type": "scale", "scale": [1.0, 1.0, 1.0, 1.0, 1.0] }] }, …
Resolution folders
Binary chunk files
OME-Zarr builds on ZARR:
Nested folder structure
Metadata text files
Binary data array chunks files
One OME-Zarr folder can contain multiple 5D images

## Slide 19
Chunks
32 x 32 x 32 vx
= 32kB for uint8
Key enabler:
Small chunks
OME-ZARR

## Slide 20
1TB = 33.554.432 files
Many 32kB files don’t play well with current file systems
OME-ZARR

## Slide 21
Idea: Put many chunks in a larger file (shard)
Header
Shard file
32 x 32 x 32 chunks
= 1GB for uint8
OME-ZARR

## Slide 22: OME-Zarr versions!
OME-Zarr 0.4
  Based on Zarr 2
    no sharding
    attribute files: .zattrs .zgroup
OME-Zarr 0.5
  Based on Zarr 3
    with sharding
    attribute files: zarr.json
  Currently does not open in Fiji 

## Slide 23: Sharing big image data with external collaborators

## Slide 25
http
ftp
…

## Slide 26: Zarr version 2 and version 3